## Slide 1: GMM-Based Multimodal Biometric Verification
Yannis Stylianou
Yannis Pantazis
Felipe Calderero
Pedro Larroy
François Severin
Sascha Schimke
Rolando Bonal
Federico Matta
AthanasiosValsamakis

## Slide 2: Outline
Introduction to Biometrics
Biometric Modalities
    Speech
    Signature
    Face
Fusion
Results
Multimodal Database
Conclusion

## Slide 3: Introduction to Biometrics

## Slide 4: Biometric Modalities: Speech

## Slide 5: Biometric Modalities: Signature

## Slide 6: Biometric Modalities: Face
Face recognition into a verification System
  Preprocessing
    Localization and segmentation
    Normalization
  Face verification
    Feature extraction
    Classification

## Slide 7: Biometric Modalities: Face
Face detection and segmentation
  Easy scenario: single user in front of the camera
  OpenCV face detector has an excellent performance

## Slide 8: Biometric Modalities: Face
Face normalization
  Position and size correction
  Based on eye detection
Binarization, inversion and eye mask selection
Detecting and selecting clusters in the upper half part
WITHOUT
Average of two images from the same user
WITH

## Slide 9: Biometric Modalities: Face
Feature extraction
  KL transform over training data  Eigenfaces
  Invariant & robust
  Computationally expansive & data dependent
Feature vector
Eigenvectors of the training covariance matrix
Vectorize image
Mean image vector

## Slide 10: Biometric Modalities: Face
Eigenfaces
  Common eigenface space
    Adding new users / images: computationally expansive
    Almost no modification for verification / identification
  Individual eigenface space
    Adding new users / new images: only recompute individual eigenfaces
    In verification system: as fast as common approach
    In identification system: operations proportional to number of users

## Slide 11: Biometric Modalities: Face
Classification
  GMM based model for each user
  Mean log-likelihood between 10 frames

## Slide 12: Fusion (I)
Modules
  Sensor Module
  Feature Module
  Matching Module
  Decision Module
Levels
  Feature Level
  Score Level
  Decision Level

## Slide 13: Fusion (II)
Matching Module
  Score Extraction
  Gaussian Mixture Models
  EM algorithm
  Actual scores => likelihoods
Decision Module
  Normalization
  Product Rule

## Slide 14: Results

## Slide 15: Multimodal Multilingual Biometric Database
The database is composed of:
  Signatures
  Video, (which generates):
    Audio
    Still pictures
  Software (scripts)
47 users / 1663 signatures / 351 videos

## Slide 16: Signatures
Signature files are composed of comma separated integer values, with
  X,Y,pressure,time
Capturing Device:
  Wacom "Graphire3 4x5" digitizer tablet. Sensing surface 127.6mm x 92.8mm. Spatial reolution is 2032 lpi (lines per inch). 512 different pressure levels. Sampling rate is about 100Hz

## Slide 17: Videos
The videos provide audio and still pictures.
  (after automated postprocessing with perl and mplayer)
Videos: uncompressed UYVY AVI 640 x 480, 15.00 fps
Audio: uncompressed 16bit PCM audio; mono, 32000Hz little endian.

## Slide 18: Controversy & Issues
Filesystem based or DB engine based (speed vs. transparency)
Raw video for better image quality or compressed video: (Octave/Matlab compatibilty, DB size...)
At some point, some users weren't willing to provide real signatures (also hypothetical legal / psychological issues were raised), we had to rebuild the signature DB at one week from the end with fakes.
Distribution of a >100 Gb database ? -> compressed videos

## Slide 19: Lessons learned
Matlab is very limited with video codecs
Bugs in postprocessing software
Raw video is HUGE
Size constraints:
  Database with raw video & raw audio: 108 Gb
  Database with mpeg2 video & raw audio: 1.8 Gb
47 users / 1663 signatures / 351 videos

## Slide 20: CONCLUSION
Constitution of a multimodal database
(thank you all  )
User verification:
- satisfactory results (EER)
- EER decreases if fusion of two modalities (voice + signature, face + signature …) - lowest if all modalities are used
First time GMM approach is used: encouraging results

## Slide 21: FUTURE WORK ?
User verification: make EER = 0 
User identification: to be developed
Enlarge database (at the moment: 47 people)
Use other features for signature authentification (currently: (x,y) coordinates ...)
Forgery: build a falsified signatures database to test the robustness of the system.
-> A signature simulator was created: signatures are reproduced in movies, at different speeds, to help the imitator.

## Slide 22: ¿ QUESTIONS ?