## Slide 1: Multimodal Multilingual Biometric Database
Speaker

## Slide 2: Multimodal Multilingual Biometric Database
The database is composed of:
  Signatures
  Video, (which generates):
    Audio
    Still pictures
  Software (scripts)
47 users / 1663 signatures / 351 videos

## Slide 3: Signatures
Signature files are composed of comma separated integer values, with
  X,Y,pressure,time
Capturing Device:
  Wacom "Graphire3 4x5" digitizer tablet. Sensing surface 127.6mm x 92.8mm. Spatial reolution is 2032 lpi (lines per inch). 512 different pressure levels. Sampling rate is about 100Hz

## Slide 4: Videos
The videos provide audio and still pictures.
  (after automated postprocessing with perl and mplayer)
Videos: uncompressed UYVY AVI 640 x 480, 15.00 fps
Audio: uncompressed 16bit PCM audio; mono, 32000Hz little endian.

## Slide 5: Controversy & Issues
Filesystem based or DB engine based (speed vs. transparency)
Raw video for better image quality or compressed video: (Octave/Matlab compatibilty, DB size...)
At some point, some users weren't willing to provide real signatures (also hypothetical legal / psychological issues were raised), we had to rebuild the signature DB at one week from the end with fakes.
Distribution of a >100 Gb database ? -> compressed videos

## Slide 6: Lessons learned
Matlab is very limited with video codecs
Bugs in postprocessing software
Raw video is HUGE
Size constraints:
  Database with raw video & raw audio: 108 Gb
  Database with mpeg2 video & raw audio: 1.8 Gb
47 users / 1663 signatures / 351 videos