## Slide 1: GMM-Based Multimodal Biometric Verification
Yannis Stylianou
Yannis Pantazis
Felipe Calderero
Pedro Larroy
François Severin
Sascha Schimke
Rolando Bonal
Federico Matta
AthanasiosValsamakis

## Slide 2: Outline
Introduction to Biometrics
Multimodal Multilingual Database
Biometric Modalities
    Speech
    Signature
    Face
Fusion
Results
Conclusions

## Slide 3: Biometrics
„Biometrics is the science of measuring physical properties of living beings.“
Two types of biometrics
  Physiological: face, fingerprints, iris…
  Behavioral: handwriting, speech…
Multimodal biometrics
  In our work, we focus on the fusion of speech, face and signature

## Slide 4: Multimodal Multilingual Biometric Database
The database is composed of:
  Signatures
  Video, (which generates):
    Audio
    Still pictures
  Software (scripts)
47 users / 1663 signatures / 351 videos
Free for the scientific community

## Slide 5: DB: Signatures
Signature files composed of comma separated integer values
  X, Y, pressure, time
Capturing Device
  Digitizer tablet

## Slide 6: DB: Videos
The videos provide audio and still pictures
  Automated postprocessing with perl and mplayer
Videos
  Uncompressed UYVY AVI 640 x 480, 15.00 fps
Audio
  Uncompressed 16bit PCM audio; mono, 32000Hz little endian.

## Slide 7: DB: Controversy & Issues
Filesystem based or DB engine based (speed vs. transparency)
Raw video for better image quality or compressed video: (Octave/Matlab compatibilty, DB size...)
Legal / psychological issuess
  Some users refuse to provide real signatures
  DB was rebuilt with fakes signatures
Compression?
  More than 100 Gb database

## Slide 8: Speech Modality
Speech signal
  20 ms frames with 10 ms frame shift
MFCC features
  Widely used in speech processing
  Robust & efficient
  First coefficient is discarded since it represents the average energy in the speech frame

## Slide 9: Signature Modality
Off-line approach
  Data acquisition after the writing process using a scanner.
  Result: 2-dimensional image
On-line approach
  Data acquisition while writing process using special devices like digitizer tablets, TabletPCs, …
  Result: time-related signals of pen movement (position, pressure, pen inclination, …)

## Slide 10: Signature Modality
We focused on on-line signatures
Device: Wacom Graphire3
  100Hz sampling rate
  x-, y-position with resolution of 2032 lpi
  512 pressure levels
Derivated features
  Angle of tangent in sample points
  Velocity

## Slide 11: Face Modality
Face recognition into a verification System
  Preprocessing
    Localization and segmentation
    Normalization
  Face verification
    Feature extraction
    Classification

## Slide 12: Face: Preprocessing
Face detection and segmentation
  Easy scenario: single user in front of the camera
  OpenCV face detector has an excellent performance

## Slide 13: Face: Normalization
Face normalization
  Position and size correction
  Based on eye detection
Binarization, inversion and eye mask selection
Detecting and selecting clusters in the upper half part
WITHOUT
Average of two images from the same user
WITH

## Slide 14: Face: Features
Feature extraction
  KL transform over training data  Eigenfaces
  Invariant & robust
  Computationally expansive & data dependent
Feature vector
Eigenvectors of the training covariance matrix
Vectorize image
Mean image vector

## Slide 15: Face: Eigenfaces
Common eigenface space
    Adding new users / images: computationally expansive
    Almost no modification for verification / identification
Individual eigenface space
    Adding new users / new images: only recompute individual eigenfaces
    In verification system: as fast as common approach
    In identification system: operations proportional to number of users

## Slide 16: Fusion
Possible levels of fusion
  Feature Level
  Score Level
  Decision Level
Matching Module
  GMM model applied to each modality
    EM algorithm
  Score extraction  log-likelihood
Decision Module
  Normalization
  Product Rule

## Slide 17: CONCLUSION
Constitution of public a multimodal database
(thank you all  )
Modality compensation
  EER decreases with the number of modalities
  Results on the final report
Homogeneous multimodal GMM approach

## Slide 18: FUTURE WORK ?
New fusion schemes
  Achieving EER = 0% ?
Development of user identification system
Enlarge the database
  At the moment: 47 people
New signatures features
Add forgeries to database
  A signature simulator for forgery training was already developed

## Slide 19: ¿ QUESTIONS ?